ARNEX PS2500

Rectangular extruded box profile 135 mm high and 150 mm wide with rounded corners at the back and bottom front. Bevel in the front lower part of the box profile. The box is mounted using mounting brackets which are fastened in grooves. The side covers are made of cast aluminium alloy. Roller 85 mm diameter in galvanized steel profile.

The system is driven by an AC tubular motor 230 V / 50 Hz.

The guide rails with SIR guide are made of aluminium and are fastened to grooves in the guide rail using clamp holders. The SIR guide ensures reliable fabric tension in all directions. When the fabric is extended, it is tensioned by gas pressure cylinders in the front profile. The front profile is made of extruded aluminium 51 mm high and 120 mm wide. Awning fabric made of Polyacrylic or PVC from the STOBAG Collection according to price list.

Option

Operating packages with RTS or io radio transmitter available.