FIXED GLAZING SYSTEM SV1051

The STOBAG profile system SV1051 offers a range of set-ups in the area of non-insulated glazing. This is suitable for use with several of our products, with roof inclines of 2° – 25°.

Type: SV1051/1	Glass piece

Type: SV1051/2	Fixed glass panel with roof pitch

Type: SV1051/3	Fixed glass panel

Type: SV1051/4	Al piece

Pivot-hung windows can be installed in the single types as an option.

The STOBAG SV1051 profile system is manufactured under licence by aliplast Aluminium Systems.

Profile system

– Non-thermally insulated/uninsulated aluminium profiles

– Installation depth 51 mm

Opening options / Fittings

Fixed glazing with pivot-hung windows can be individually extended as an option.

Tilt windows

1-leaf tilt windows are optionally available.

– Opening to inside

– Leaf widths 400 to 1300 mm

– Leaf heights 410 to 1600 mm

– Installation in type SV1051/1, SV1051/2 and SV1051/3 possible

– Standard fittings anodised colourless comprising:
Tilt fittings
Skylight catch

Impermeability and Ventilation

– Rain and wind impermeability is guaranteed by EPDM seals

Glazing

– Standard glass laminated safety glass (USG) 8-2 with clear or matt foil

– Panes can be easily changed at a later date

Planning / Orders

– Planning and orders are material-related and may vary