SECURE FL1000

The security shutter has a firmly connected lamella armour which folds into the end rail from bottom to top, with a bevel gearbox 3.5:1 and buckle operating handle or, if more than 4 m, with a motor. The top suspension profile, with adjustable height, fixes the armour in the guide rails. The end rail is connected to the drive rails with a chrome steel angle and is therefore a firm connection element. Both extruded aluminium lamellas (full profile) are connected with a hinge bar and are, due to the dented form, a strong unity. The bottom lamella has an end nose which, when closed, does not offer any surface for assaults. The drive guide is fitted with a push chain drive which stays locked in any position. The guide rail integrated in the drive rail is adjustable and holds the hinge bars with snap-on plastic gliders, thus guiding the aluminium lamella armour. The drive connection of both guide rails from left to right is done with a steel shaft and hollow shaft with spring link unit by the chain tail sheave on the upper part of the guide rail.

Option

Gearbox execution with operating handle link and detachable buckle operating handle with operating handle funnel.

The ES-guide rail has a hollow cavity profile in which the bevel gearbox 3.5:1 can be integrated. This execution is necessary if no gearbox niche exists.

Electric drive

AC-motor 220/230 V – with electromagnetic brake and electronic end stop, thermo protection IP54 (splash water), with cable 0.8m 4-poles feeder connection cable.