SIGMA S7000

Folding arm awning with operating handle. Fabric cover. Retraction and extension with detachable operating handle. Bevel gearbox with gearbox reduction 4.6:1. Awning without mounting bar. Combined brackets for top fixing, arm fixation and support for roller tube. Folding arms made of extruded aluminium profiles, with precision joints made of cast aluminium. Integrated tension springs and stainless steel cables and cable protection sleeves over the middle joint. Roller tube made of galvanised steel with groove for the cover fixation. Combined brackets with security against knock-ups and adjustable incline. Brackets for top fixing only. Front rail made of extruded multiple chamber aluminium profile with end caps, grooves for the cover and the valance, with ­fixation groove for the folding arms. Operating handle powder coated matching the standard colours, with hook and plastic handle.

Option electric drive

Tubular AC motor 230 V / 50 Hz with friction brake and electronic end stop. Thermal protection. Protection class IP54 (splash water), with 50 – 150 cm 4-pole connection cable.